## Slide 1
Router and Routing Basics

## Slide 2: Routing Protocols and Concepts
Routing and packet forwarding
Static routing
Dynamic routing protocols
Distance vector routing protocols
Link-state routing protocols

## Slide 3: Routers
Special type of computer
Connect and allow communication between two networks
Determine the best path through the network
Configuration files to control the traffic
Generally have two connection types:
  WAN connection (connection to ISP)
  LAN connection

## Slide 4: Routers
Data is sent in form of packets between two end devices
Routers are used to direct packets to its destination
Routers examine a packets destination IP address and determine the best path by using a routing table

## Slide 5: Cisco IOS Software
Operating system in all of the Cisco routers or switches, which provides the following network services:
Basic routing and switching functions
Reliable and secure access to networked resources
Network scalability

## Slide 6: Router components
CPU
  Executes operation systems instructions
RAM
  Stores instructions and data needed for CPU
ROM
  Boot instructions, scaled-down vers. of IOS
Flash
  Stores IOS, copied into RAM during bootup proc.
NVRAM
  Startup configuration file

## Slide 7: Router Boot-up process
Major phases to the router boot-up process
  Test router hardware
    Power-On Self Test (POST)
    Execute bootstrap loader
  Locate & load Cisco IOS software
    -Locate IOS
    -Load IOS
  Locate & load startup configuration file or enter setup mode
    -Bootstrap program looks for configuration file

## Slide 8: IOS File System Overview

## Slide 9: Router interfaces
Interface: a physical connector on the router, main purpose to receive and forward packets
Interfaces connects to various types of networks, and different types of media and connectors are required
Each interface connects to a separate network

## Slide 10: Router interfaces
LAN interfaces
  Ethernet, fastEthernet
  Connects the router to a LAN
WAN interfaces
  Serial, ISDN, Frame Relay
  Connects the router to external networks, interconnect LANs

## Slide 11: Routing
Process to forward packets to destination networks
Layer 3 device
Examines destination IP address (Layer 3)
Routing table is used to find best path to destination

## Slide 12: Routing
Forwarding decisions based on Layer 3
Operates at Layer 1, 2 and 3

## Slide 13: Routing Table
Data file in RAM
Stores information about directly connected and remote networks
Contains network/next hop associations
Directly connected networks
Remote networks
  Static routes (manually configured)
  Dynamic routing protocols (learned from other routers)

## Slide 14: Static Routing
Configured manually
Specifies network address and subnet mask of remote network, and IP address of next hop router or exit interface
Use static routes when:
  Network only consists of few routers
  Network is connected to Internet only through one ISP

## Slide 15: Static Routing
Advantages:
Minimal CPU processing
Easy to configure
Easier for administrator to understand

## Slide 16: Static Routing
Disadvantages:
Configuration and maintenance is time- consuming
Does not scale well with growing networks
Requires complete knowledge of the whole network for proper implementation

## Slide 17: Static Routing

## Slide 18: Dynamic routing
Added to routing table by using a dynamic routing protocol
Used by routers to share information about the reachability and status of remote networks
Perform several activities:
  Network discovery
  Updating and maintaining routing tables

## Slide 19: Dynamic routing
Advantages:
Less administrative overhead when adding or deleting a network
Protocols automatically react to the topology changes
More scalable

## Slide 20: Dynamic Routing
Disadvantages:
Router resources are used (CPU cycles, memory and link bandwidth)
More administrator knowledge is required for configuration, verification and troubleshooting

## Slide 21: Dynamic Routing

## Slide 22: Best Path and Metric
Multiple path to same destination
Best path is selected by the routing protocol, based on a specific value (metric)
Each protocol uses its own rules and metrics to build and update routing tables
Metric is used to measure the distance to the destination network
Lowest metric = best path, placed in routing table

## Slide 23: Metrics
Hop cont: counts the number of routers a packet must traverse
Bandwidth: preferring the path with highest bandwidth
Load: traffic utilization on a link
Delay: time for a packet to traverse a path
Reliability: probability of a link failure
Cost: determined by IOS or administrator to indicate preference for a route

## Slide 24: Path Determination
The process of how the router determines which path to use when forwarding a packet
Directly connected
  Forwarded directly to the destination
Remote network
  Forwarded to another router
No route determined
  Packet discarded, ICMP unreachable sent

## Slide 25: Switching Function
Process used by a router to accept a packet on one interface and forward it out another interface
Decapsulate the Layer 3 packet by removing Layer 2 frame header and trailer
Examines destination IP address of the packet to find best path in routing table
Encapsulate Layer 3 packet into a new Layer 2 frame and forwards on correct interface

## Slide 26: Example
PC 1 will send a packet to PC 2

## Slide 27: Example cont.

## Slide 28: Example cont.

## Slide 29: Example cont.

## Slide 30: IP Routing protocol
RIP (Routing Information Protocol)
IGRP (Interior Gateway Routing Protocol)
EIGRP (Enhanced IGRP)
OSPF (Open Shortest Path First)
IS-IS (Intermediate System-to-Intermediate System)
BGP (Border Gateway Protocol)

## Slide 31: Autonomous System (AS)
32
Version 2
002-1 © 2002, Svenska-CNAP / Halmstad University.
Collection of networks/routers
Share a common routing strategy
Viewed as a single entity from the outside world

## Slide 32: Routing Protocols
Routing protocols can be classified into different groups according to their characteristics
  Interior Gateway Protocols (IGP)
  Exterior Gateway Protocols (EGP)
32

## Slide 33: IGP Routing Protocols
33
Two classes of routing protocols:
Distance vector
  Determines the direction and distance to any link in the internetwork
Link-state
  Recreates the exact topology of the entire internetwork

## Slide 34: Distance Vector Routing Protocol
34
Periodic updates
Slow convergence
Routing table from directly connected neighbor routers
Add distances before passing it to other neighbors
Distance is defined in terms of a metric, such as hop count

## Slide 35: Link-state Routing Protocol
35
Complex database of topology information
Knowledge of the entire network
Uses SPF to calculate the best path
Updates when changes in the topology occurs
Fast Convergence
More memory and processor overhead

## Slide 36: Classful Routing Protocols
36
Do not send subnet mask information in routing updates
Do not support variable length subnet masks (VLSM) and discontiguous networks

## Slide 37: Classless Routing Protocols
37
Include the subnet mask in routing updates
Supports both VLSM and discontiguous networks
Required in most networks today

## Slide 38: Classful vs. Classless Routing
38

## Slide 39: Convergence
39
When all routers routing tables are at a state of consistency
All routers have complete and accurate information about the network
Convergence time is the time it takes routers to share information, calculate best paths, and update their routing tables
A network is not completely operable until the network has converged. Short convergence times are required

## Slide 40: Load Balancing
The ability for a router to distribute packets among multiple same cost paths
40

## Slide 41: Administrative Distance
Administrative distance is used to determine the best path to a particular destination, when the same path is learned from two or more different routing sources
Measures the trustworthiness of a routing source
Lowest AD is inserted in the routing table
41

## Slide 42: Default Routes
42
Used when the router is unable to match a destination network
Do not have to maintain a routing table entry for every Internet network
Statically entered by an administrator
– ip route 0.0.0.0 0.0.0.0
Dynamically learned using a routing protocol
– ip default-network